ALLEN ORTHOTICS AND PROSTHETICS

2502 West Ohio Avenue						1921 East 37th Street, Suite A Midland, Texas							                         Odessa, Texas

432-683-3788								                           432-332-9821

Donning and Care for Your Knee Ankle Foot Orthosis (KAFO)

Function:

Your KAFO is designed to accommodate or correct a deformity or to provide support to your lower extremity.

Use:

Donning Your KAFO

- Always wear a sock when wearing the orthosis. This will aid in preventing skin break down by reducing pressure.

- Put the KAFO on by placing your foot and leg inside the brace from the front opening.

- Make sure that your heel is fully down in the orthosis. If there is space between your heel and the bottom of the orthosis, this could cause skin break down. An easy way to get your heel into the orthosis properly is to bend your knee to 90 and press down on the top of your knee with moderate force. This will push your heel down, insuring full contact.

- At this time, tighten the strap(s) of your orthosis to the mark that was established by your Orthotist at the time of fitting. If marks were not made as a reference point, tighten the straps down snuggly but still allowing for circulation to your feet.

- Place your shoe over your orthosis and foot, making sure again that your toes stay extended. Tie your shoe snuggly to prevent movement between the orthosis and the shoe.

- If your orthosis has knee joint locks, take extra care to insure that the locks are fully engaged before walking and that the locks are fully disengaged before sitting.

Wear Schedule for Your Orthosis

You will use a progressive wear schedule to insure that your skin becomes accustomed to your new orthosis.  Wear your new orthosis for no more than one hour at any one time on the first day you receive it. Gradually increase your wearing time by one hour until you are wearing the orthosis for an entire day without any difficulty.  It is extremely important to monitor your skin for any redness that does not dissipate within 20-30 minutes.  If problems arise, such as excessive pressure or redness discontinue use and contact our office.  If skin breakdown occurs discontinue use and contact your physician immediately.

Care/Maintenance

You can clean the inside of your plastic orthosis with rubbing alcohol applied lightly with a clean towel. Allow the alcohol to dry fully before donning the orthosis. If your orthosis has leather, a leather cream, found in most shoe store, should be used for cleaning. Allow cream to fully dry before donning the orthosis.

Precautions

Check your skin for redness over boney areas immediately after taking your KAFO off.  Also check skin in areas corresponding to the edges of the orthosis, and the edges of the strap(s). Areas of redness should dissipate within 20-30 minutes. If the red areas do not dissipate contact our office and schedule and appointment for an adjustment to be made. If you experience skin breakdown, discontinue use and contact your physician for an appointment to have the area assessed.  Avoid using lotions on your skin as this will soften the tissue. Soft skin is more susceptible to skin break down.

Report failures, malfunctions or changes in your physical condition to us as soon as possible.