ALLEN ORTHOTICS AND PROSTHETICS

2502 W. Ohio Avenue							1921 E. 37th Street, Ste. A

Midland, TX										Odessa, TX

432-683-3788										432-332-9821

Use and Care for Your Knee Ranger

Function:

Your knee Ranger is designed to limit flexion and/or extension for post-op/post-injury control or immobilization.

Use:

Donning Your Knee Orthosis

- Prior to donning your orthosis, your Orthotist will contour the side bars to fit your leg shape.

- Also, the degree of flexion/extension will be set and locked according to the physician’s recommendation.

- First, check that the wrap is at the right height and angle by closing it without strapping. If it is in the correct position your knee cap should be in the center of the front opening. If it is not, adjust the wrap accordingly.

- Next make sure that the knee hinges are on either side of the anatomical knee center.

- Close the straps snuggly. You do not want to cut off circulation to your foot; however, the tighter the straps are the more control there will be against unwanted motion.

Wear Schedule

Follow the wear schedule provided by your prescribing physician. If one was not discussed, call the physician’s office for a recommendation.

Care/Maintenance:

Your orthosis may be hand washed with mild soap, triple rinsed, squeezed and air dried. The uprights may be removed for washing. Prior to removal you should mark their location with a marker onto the foam wrap to ensure that they are returned to the correct position.

Precautions:

Do not over tighten the straps as this could lead to an increase in swelling and pain.

Report failures, malfunctions or changes in your physical condition to us as soon as possible.