ALLEN ORTHOTICS AND PROSTHETICS

2502 West Ohio Avenue						1921 East 37th Street, Suite A Midland, Texas							                         Odessa, Texas

432-683-3788								                           432-332-9821

Donning and Care for Your Ankle Foot Orthosis (AFO)

Metal AFO

Function:

Depending on your condition, your AFO is designed to correct or accommodate a deformity, provide support to your foot /ankle and/or assist you in walking.

Use:

Donning Your Metal AFO

- Apply a sock to your foot and leg that is at least as tall as the orthosis. This will aid in preventing skin break down by eliminating edge pressure from the sock. You may also find that this is a more comfortable way to wear your orthosis.

- Don the brace by placing your foot inside your shoe and your leg into the metal section. Your calf should be in contact with the leather lined band at the top of the orthosis.

- Make sure that your heel is fully down into the shoe. If there is space between your heel and the bottom of the shoe, this could cause skin break down. An easy way to get your heel into the shoe properly is to bend your knee to 90 and press down on the top of your knee with medium force. This will push your heel down insuring full contact.

- Make sure that your toes have not become bent while your were donning your shoe. An easy way to check is feel your toes from the out side of the shoe with your hand, you should feel all five toes laying flat against the insole of the shoe.

- At this time, tighten the strap(s) of your orthosis to the mark that was established by your Orthotist at the time of fitting. If marks were not made as a reference point, tighten the straps down snuggly but still allowing for circulation to your feet.

- Tie your shoe snuggly to prevent movement between you and the orthosis.

Wear Schedule for Your Orthosis:

You will use a progressive wear schedule to insure that your skin becomes accustomed to your new orthosis.  Wear your new orthosis for no more than one hour at any one time on the first day you receive it. Gradually increase your wearing time by one hour until you are wearing the orthosis for an entire day without any difficulty.  It is extremely important to monitor your skin for any redness that does not dissipate within 20-30 minutes.  If problems arise, such as excessive pressure or redness discontinue use and contact our office.  If skin breakdown occurs discontinue use and contact your physician immediately.

Care/Maintenance

- ( if applicable) The leather lining around the calf band can be spot cleaned with a mild soap and water, but should be allowed to completely dry before the orthosis is re-applied. If you desire, a leather cleaner can be used instead.

- Your shoe can be cleaned with soap and water; allow ample time to dry before re-applying.

Precautions:

Check your skin for redness over boney areas immediately after taking your AFO off.  Also check skin in areas corresponding to the edges of the orthosis, and the edges of the strap(s). Areas of redness should dissipate within 20-30 minutes. If the red areas do not dissipate contact our office and schedule and appointment for an adjustment to be made. If you experience skin breakdown, discontinue use and contact your physician for an appointment to have the area assessed.  Avoid using lotions on your skin as this will soften the tissue. Soft skin is more susceptible to skin break down.

Report failures, malfunctions or changes in your physical condition to us as soon as possible.