ALLEN ORTHOTICS AND PROSTHETICS

2502 West Ohio Avenue					                  1921 East 37th Street, Suite A

Midland, Texas							                              Odessa, Texas

432-683-3788								                               432-332-9821

NEOPRENE  SUSPENSION SLEEVE

USE AND CARE

Function:

A Neoprene suspension sleeve is used to provide primary suspension of a transtibial prosthesis.

Use:

Donning the Neoprene suspension sleeve:

# The top part of the sleeve should come in direct contact with the skin of the thigh and should extend at least 4 to 6 inches above the top of the prosthetic socks.

- The 2 horizontal seams on the sleeve should be located above and below the socket edge. This places the reinforced area of the sleeve over the socket edge and prevents premature wear of the sleeve.

- Take care when pulling the sleeve up onto the thigh area.

- DO NOT overstretch.

# Be careful with fingernails, which can damage the sleeve.

Care & Maintenance:

Hygiene:

- Clean the inside neoprene surface with alcohol at the end of each day to prevent bacterial growth and irritation. Do not soak the sleeve in alcohol.

- To clean the outside of the sleeve hand wash with non-detergent soap and water.

- Let the sleeve air dry completely before reapplying to the prosthesis.

Precautions:

  - If you experience skin irritation, rash or excessive itching when using a suspension sleeve you should evaluate your cleaning methods and products before seeking the advice of your prosthetist and/or dermatologist.

  - Do not leave the sleeve turned down over the socket when the prosthesis is not being worn. This will cause the top of the sleeve to become stretched

Report failures, malfunctions or changes in your physical condition to us as soon as possible.