ALLEN ORTHOTICS AND PROSTHETICS

2502 West Ohio Avenue						1921 East 37th Street, Suite A Midland, Texas							                         Odessa, Texas

432-683-3788								                           432-332-9821

APPLICATION INSTRUCTIONS FOR AK PROSTHESIS

WITH LOTION FIT

Application of the Prosthesis:

- Apply a small amount of lotion to the flexible socket and the residual limb.  Your pull sock is then placed inside the socket with the split end hanging over the inside wall of the socket by about 3 inches, the un-split end should be coming out of the valve hole.

- The limb is then placed into the socket with the correct rotation.  The adductor longus tendon should line up in the channel in the top inside corner of the socket.  Weight is applied to the socket and the pull sock is pulled out of the valve hole.

- As the pull sock gets tight, lift up out of the socket slightly and then put weight back into the socket.  This pistoning action works well while pulling out the sock.  The pull sock helps ease the soft tissues of the inner thigh into the socket.

- There should be no space between the residual limb and the socket after the sock is removed.

- Install the valve.

Report failures, malfunctions or changes in your physical condition to us as soon as possible.