ALLEN ORTHOTICS AND PROSTHETICS

2502 West Ohio Avenue					                     1921 East 37th Street, Suite A

Midland, Texas							                                 Odessa, Texas

432-683-3788								                                   432-332-9821

URETHANE GEL LINER WITH NO OUTER COVER 
USE AND CARE

Check with your prosthetist to determine which gel liner you have been fitted with before following the directions below.

Function:

The Urethane Cushion Liner is used to reduce shear and friction forces and to provide cushion to residual limb.

Use:

For Liners Without Outer Fabric Covers:

- Your residual limb should be clean, dry and free of soap residue.  Products containing petroleum jelly will damage the liner and should be avoided.  Do not use baby powder on limb or liner.

- Invert the liner inside out so that the inside surface is on the outside, then spray a small amount of soapy water or skin-friendly lotion inside the liner, Do Not Use Alcohol.  Rub the liner walls together to spread around the soapy water or lotion. This lubricant will make it much easier to apply the liner.

- With the logo in the front (if applicable), place the end of the liner directly against the end of your residual limb.  Carefully roll the liner up your limb with the gel side against the skin. The lubrication should allow the liner to slide against itself and roll onto your limb more freely.  The lubricated surface should not be against your skin.   Make sure that the liner is rolled, not pulled.  Pulling the liner on will stretch the skin and cause irritation.

- Make sure that there are no wrinkles or air pockets between your limb and the liner by sliding your hands from the bottom of the liner to the top a few times to burp out any trapped air. The liner should be in complete contact with the end of your limb.

- Use non-medicated A&D ointment or Sensi~Care body cream if you need a lubricant between your skin and the urethane liner.

- Don your prosthesis.

- Apply and adjust your prosthetic sock ply to make up the correct volume so your prosthesis fits                   snugly.

Perspiration:

- It is not unusual for new gel liner wearers to experience excessive perspiration during the first several weeks of use.

- The application of unscented antiperspirant to the residual limb is an effective method of controlling sweating.  The unscented antiperspirant should be applied at night after removing the liner and cleaning the residual limb.  Application of the antiperspirant at night gives the antiperspirant time to evaporate before donning the liner and prosthesis the next morning.

- Never use these products on open sores.

- New wearers can remove and dry their liners once or twice a day to reduce the accumulation of perspiration inside the liner.

Care & Maintenance

Cleaning: The liner must be thoroughly cleaned at the end of each day and should be allowed to dry before

reapplying.

- Occasionally, liners are issued in pairs so that you can wear one while cleaning and drying the other.

- Use mild body soap such as unscented Ivory for cleaning the liner and your residual limb. Skin reactions have been observed when using deodorant, anti-bacterial, and perfumed soaps and lotions.

- If you experience a skin reaction when using a gel liner you should evaluate your cleaning methods and products before seeking the advice of your prosthetist and/or dermatologist.

Daily Cleaning:

1.	Remove the liner by rolling it off your residual limb, it will now be inside out.

2.	Immediately after removing the liner, clean the liner with hot water and unscented mild hand soap, Do Not Use Alcohol.  Apply the soap by hand or with a clean, soft cloth or sponge.  Note: Do not scrub the liner which can roughen the surface and irritate your skin.

3.	Take special care to rinse all soap residue from the liner.

4.	Gently dry liner with a lint free cloth and reverse so that outside of the liner is now on the outside (in the wearing position).

5.	Lay flat to dry with outside surface on the outside.

6.	Clean your residual limb.

Precautions:

Do not wear the liner overnight.  Your limb needs to be cleaned once a day and exposed to the air for several hours.  If you experience skin irritation, rash or excessive itching when using a gel liner you should evaluate your cleaning methods and products before seeking the advice of your prosthetist and/or dermatologist.

Storing the Liner:

- When the liner is not being worn, it should be stored on the drying stand or laying flat in a cool, dry place, fabric side out.

- If the liner will not be used for an extended period, cover the dry liner with a clean plastic bag.

- It is not advisable to keep the liner folded or rolled up when not in use as this may cause permanent creases.

Report failures, malfunctions or changes in your physical condition to us as soon as possible.